## Slide 1: ARP Poisoning
S.Venkatesan
Indian Institute of Information Technology, Allahabad

## Slide 2: Acknowledgement: The contents and figures are copied from various sources. Thanks to all authors and sources made those contents public and usable for educational purpose

## Slide 3: Slides from
Lecture 20: Routing Security (Hijacking the Internet for fun and profit!), CSE390 – Advanced Computer Networks
Steve Kent, Security the Border Gateway Protocol using S-BGP
Slides of Prof. Sandeep Kumar Shukla
https://slideplayer.com/slide/2547379/

## Slide 4: Introduction
A computer connected to an IP/Ethernet has two addresses
  Address of network card (MAC address)
    Globally unique and unchangeable address stored on the network card.
    Ethernet header contains the MAC address of the source and the destination computer.
  IP address
    Each computer on a network must have a unique IP address to communicate.
    Virtual and assigned by software.

## Slide 5: Introduction
IP communicates by constructing packets.
Packet are delivered by Ethernet.
  Adds an Ethernet header for delivery
  Splits the packets into frames
  Sends them down the cable to the switch.
  The switch then decides which port to send the frame to. By comparing the destination address of the frame to an internal table which maps port numbers to MAC addresses.

## Slide 6: Introduction
When an Ethernet frame is constructed from an IP packet, it has no idea what the MAC address of the destination machine is.
The only information available is the destination IP address.
There must be a way to the Ethernet protocol to find the MAC address of the destination machine, given a destination IP.
This is where ARP, Address Resolution Protocol, come in.

## Slide 7
Address resolution and Reverse address resolution

## Slide 10
Encapsulation of ARP

## Slide 11: ARP process
  Get IP address of target.
  Create a request ARP message
    Fill sender physical address
    Fill sender IP address
    Fill target IP address
    Target physical address is filled with 0
  The message is passed to the data link layer where it is encapsulated in a frame.
    Source address: physical address of the sender.
    Destination address: broadcast address.

## Slide 12: ARP process
  Every host or router on the LAN receives the frame.
    All stations pass it to ARP.
    All machines except the one targeted drop the packet.
  The target machine replies with an ARP message that contains its physical address.
    A unicast message.
  The sender receives the reply message and knows the physical address of the target machine.

## Slide 15
Figure 8-9

## Slide 17: ARP Cache
  To avoid having to send an ARP request packet each time, a host can cache the IP and the corresponding host addresses in its ARP table (ARP cache).
  Each entry in the ARP table is usually “aged” so that the contents are erased if no activity occurs within a certain period.
  When a computer receives an ARP reply, it will update its ARP cache.
  ARP is a stateless protocol, most operating systems will update their cache if a reply is received, regardless of whether they have sent out an actual request.
https://superuser.com/questions/1345144/what-is-the-default-cache-refresh-rate-of-windows-8-and-ubuntu

## Slide 18: ARP Spoofing
Construct spoofed ARP replies.
A target computer could be convinced to send frames destined for computer A to instead go to computer B.
Computer A will have no idea that this redirection took place.
This process of updating a target computer’s ARP cache is referred to as “ARP poisoning”.

## Slide 19
A
IP:10.0.0.1
MAC:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc

## Slide 20
A
IP:10.0.0.1
MAC:aa:aa:aa:aa
B
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
A’s cache is poisoned

## Slide 21: ARP Spoofing
Now all the packets that A intends to send to B will go to the hacker’s machine.
Cache entry would expire, so it needs to be updated by sending the ARP reply again.
  How often?
  depends on the particular system.
  Usually every 40s should be sufficient.
In addition the hacker may not want his Ethernet driver talk too much

## Slide 22: Man-in-the-Middle Attack
A hacker inserts his computer between the communications path of two target computers.
The hacker will forward frames between the two target computers so communications are not interrupted.
E.g., Hunt, Ettercap etc.
  Can be obtained easily in many web archives.

## Slide 23
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | bb:bb:bb:bb
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc
Spoofed ARP reply
IP:10.0.0.2
MAC:cc:cc:cc:cc

## Slide 24
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
T1’s cache is poisoned

## Slide 25
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | aa:aa:aa:aa
ARP cache
Forged ARP replies
IP:10.0.0.1
MAC:cc:cc:cc:cc
Forged ARP replies
IP:10.0.0.1
MAC:cc:cc:cc:cc

## Slide 26
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
T2’s cache is poisoned

## Slide 27
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
Message intended to send to T2
Hacker will
relay the
message

## Slide 28
T1
IP:10.0.0.1
MAC:aa:aa:aa:aa
T2
IP:10.0.0.2
MAC:bb:bb:bb:bb
Hacker
IP:10.0.0.3
MAC:cc:cc:cc:cc
switch
IP | MAC
10.0.0.2 | cc:cc:cc:cc
ARP cache
IP | MAC
10.0.0.1 | cc:cc:cc:cc
ARP cache
Hacker will relay the message
Message
intended to
send to T1

## Slide 29: Possible types of attacks
  Sniffing
    By using ARP spoofing, all the traffic can be directed to the hackers.
    It is possible to perform sniffing on a switched network now.
  DoS
    Updating ARP caches with non-existent MAC addresses will cause frames to be dropped.
    These could be sent out in a sweeping fashion to all clients on the network in order to cause a Denial of Service attack (DoS).
  Hijacking
    By using MiM attack, all the traffic of a TCP connection will go through the hacker.
    Now it is much easier to hijack the session as compared to the other methods.

## Slide 30: Possible types of attacks
  Broadcasting
    Frames can be broadcast to the entire network by setting the destination address to FF:FF:FF:FF:FF:FF (broadcast MAC).
    By sweeping a network with spoofed ARP replies which set the MAC of the network gateway to the broadcast address, all external-bound data will be broadcast, thus enabling sniffing.
    If a hacker listen for ARP requests and generate reply with broadcast address, large amounts of data could be broadcast on the networks.
  Cloning
    A MAC address is supposed to be unique.
    It is possible to change the MAC address of a network card (burn into the ROM).
    It is also possible to change the MAC on the OS level in some OS.
      ifconfig
    An attacker can DoS a target computer, then assign themselves the IP and MAC of the target computer, thus he can receive all frames intended for the target.

## Slide 31: Defenses against ARP Spoofing
No Universal defense.
Use static ARP entries
  Cannot be updated
  Spoofed ARP replies are ignored.
  ARP table needs a static entry for each machine on the network.
  Large overhead
    Deploying these tables
    Keep the table up-to-date
  Someone point out Windows still accepts spoofed ARP replies and updates the static entry with the forged MAC.
    Sabotaging the purpose of static routes.
Port Security
  Also known as port binding or MAC Binding.
  A feature on some high-end switches.
  Prevents changes to the MAC tables of a switch.
    Unless manually performed by a network administrator.
  Not suitable for large networks and networks using DHCP.

## Slide 32: RARP (Reverse ARP)
  Requests the IP of a known MAC.
  Detect MAC cloning.
  Cloning can be detected, if multiple replies are received for a single RARP.

## Slide 33: Gratuitous ARP
  Source and target IPs in the ARP request are the same.
  In form of broadcast.
  Some implementations recognize it as a special case, that of a system sending out updated information about itself to everybody, and cache that request.
  One packet can screw up the entire network.

## Slide 34: DAI
Dynamic ARP Inspection (DAI) is a security feature that protects ARP (Address Resolution Protocol) which is vulnerable to an attack like ARP poisoning.
DAI checks all ARP packets on untrusted interfaces, it will compare the information in the ARP packet with the DHCP snooping database and/or an ARP access-list. If the information in the ARP packet does not match, it will be dropped.
https://networklessons.com/switching/dai-dynamic-arp-inspection

## Slide 35: DHCP Snooping
Source - https://community.fs.com/blog/what-is-dhcp-snooping-and-how-it-works.html

## Slide 36: MACSec
MACsec is a Layer 2 protocol that relies on GCM-AES-128 to offer integrity and confidentiality, and operates over ethernet.
It can secure all traffic within a LAN, including DHCP and ARP, as well as traffic from higher layer protocols.
It is an extension to 802.1X provides secure key exchange and mutual authentication for MACsec nodes.
IPsec (a Layer 3 security protocol) and TLS (a Layer 4 security protocol) offer different guarantees and can be a better fit, depending on the use case.
Ref: https://developers.redhat.com/blog/2016/10/14/macsec-a-different-solution-to-encrypt-network-traffic

## Slide 37: MACSec

## Slide 38: References
https://www.ndss-symposium.org/wp-content/uploads/2017/09/Secure-Border-Gateway-Protocol-S-BGP.pdf
https://www.vpnfaqs.com/vpn-protocols-whats-the-best/
https://privacyaustralia.net/vpn-protocols/
https://zicodeng.medium.com/how-vpn-works-b7549dcc6ce4